## Slide 1
RackBlox: A Software-Defined Rack-Scale Storage
System with Network-Storage Co-Design
Benjamin Reidys
Yuqi Xue Daixuan Li Bharat Sukhwani*
Wen-mei Hwu Deming Chen Sameh Asaad* Jian Huang
*

## Slide 2
Software-Defined Infrastructure is Increasingly Popular
Systems Platform Research Group at UIUC
Top of Rack (ToR) Switch
Clients
…
Storage Server
Storage Server
Software-Defined
Networking
Software-Defined Storage
Redefine
management policies
Adopted in major data centers

## Slide 3
What is Software-Defined Networking?
Systems Platform Research Group at UIUC
Data Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Congestion Control
Customized packet format
Customized packet processing
Flexible traffic management
Programmable Switch
Control Plane

## Slide 4
What is Software-Defined Storage?
Systems Platform Research Group at UIUC
Storage Server
Allow software to manage storage chips

## Slide 5
Background on Solid-State Drives
Systems Platform Research Group at UIUC
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Data Plane
Read
Write
Erase
Storage Server
Increasing performance
Decreasing Cost
Garbage collection for out-of-place updates
Wear leveling distributes writes across flash blocks
Allow software to manage storage chips

## Slide 6
What is Software-Defined Flash?
Systems Platform Research Group at UIUC
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Data Plane
Read
Write
Erase
Storage Server
Improved resource utilization
Predictable storage performance
Allow software to manage storage chips

## Slide 7
SDN/SDF are Managed Separately Today
Systems Platform Research Group at UIUC
Data Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Congestion Control
Software-Defined Networking
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Data Plane
Read
Write
Erase
Storage Server
Software-Defined Flash
Control Plane

## Slide 8
Research Problem: Lack of Coordination between SDN/SDF
Systems Platform Research Group at UIUC
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Congestion Control
Read
Write
Erase
Conflicting policies!
Missed opportunities for rack-scale optimization!
Software-Defined Networking
Data Plane
Data Plane
Software-Defined Flash
Redundant effort!
Control Plane

## Slide 9
Research Problem: Lack of Coordination between SDN/SDF
Systems Platform Research Group at UIUC
…
Does not leverage existing data replicas during GC!
Different SSDs may have different write traffic!
Data is replicated by default!
SSDs wear out an uneven rate!
Switch is the central hub for all I/O requests!

## Slide 10
Research Problem: Lack of Coordination between SDN/SDF
Systems Platform Research Group at UIUC
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Congestion Control
Read
Write
Erase
Conflicting policies!
Missed opportunities for rack-scale optimization!
Software-Defined Networking
Data Plane
Data Plane
Software-Defined Flash
Redundant effort!
Control Plane
SDN and SDF should coordinate!

## Slide 11
RackBlox: A Software-Defined Rack-Scale Storage System
Systems Platform Research Group at UIUC
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Congestion Control
Read
Write
Erase
Data Plane
Data Plane
RackBlox
Decouple storage management
Enable rack-scale wear leveling
Enable coordinated garbage collection
Enable coordinated I/O scheduling
Coordinated I/O
Scheduling
Local I/O
Scheduling
Coord. Garbage
Collection
Global Wear
Leveling
Local Garbage Collection
Local Wear Leveling
Control Plane

## Slide 12
Enabling SDN/SDF Codesign is Challenging
Systems Platform Research Group at UIUC
How to decouple the storage management
Limited hardware resources in the switch
Ensure flexibility and
ease-of-use
SDF
SDN
Storage Management

## Slide 13
Decoupling the Storage Management Across SDN/SDF
Systems Platform Research Group at UIUC
Storage Management in SDN
vSSD_ID | GC Status | Server IP
vSSD1 | 1 | 10.0.0.16
vSSD2 | 0 | 10.0.0.20
vSSD_ID | GC Status | Replica vSSD_ID
vSSD1 | 1 | vSSD12
vSSD2 | 0 | vSSD20
Storage Management in SDF
…
vSSD #1
vSSD #2
vSSD #3
Flash Channels
Benefit from coordination
State retained in switch?
13
Storage Functions
I/O Scheduling
Garbage
Collection
Wear
Leveling
Bad Block Management
Address Translation
ECC

## Slide 14
Customized packet for RackBlox
Systems Platform Research Group at UIUC
ETH | IP | TCP/UDP | OP | vSSD_ID | Latency | Payload
OP code | Operation Name | Description
000 | create_vssd | Register new vSSD in switch
001 | del_vssd | Remove vSSD from switch
010 | write | Client write
011 | read | Client read
100 | gc_op | Packet to update GC in switch
State Communication Between SDN/SDF
Requires no hardware changes!

## Slide 15
Systems Platform Research Group at UIUC
Network Delay
Network Delay
Request #1
Request #2
Storage Delay
Storage Delay
SLO Latency
Enabling Coordinated I/O Scheduling
Storage Delay
Request Delay
Storage Queue
Request #2
I/O Request
I/O Request
Request #1
In-Network Telemetry
Storage Queuing Delay
Sliding Window Predictor
+
+
=
Storage Delay

## Slide 16
Enabling Coordinated Garbage Collection
Storage Request
vSSD_ID | GC Status
vSSD | 1
Replica | 0
Redirect request
VSSD_ID | Server IP
vSSD | 10.0.0.16
Replica | 10.0.0.20
A
B
Check switch tables
Systems Platform Research Group at UIUC
GC can add significant storage delay!
Replica
vSSD

## Slide 17
Enabling Coordinated Garbage Collection
vSSD_ID | GC Status
vSSD | 1
Replica | 0
Systems Platform Research Group at UIUC
Storage Requests
vSSD_ID | GC Status
vSSD | 1
Replica | 1
Can I do GC now?
VSSD_ID | Server IP
vSSD | 10.0.0.16
Replica | 10.0.0.20
vSSD_ID | GC Status
vSSD | 0
Replica | 0
A
B
Check switch tables
C
No, GC delayed!
vSSD_ID | GC Status
vSSD | 0
Replica | 1
C
Yes, GC executes!
Replicas may execute GC simultaneously
Replica
vSSD
GC finished

## Slide 18
Enabling Coordinated Garbage Collection
Systems Platform Research Group at UIUC
Storage Requests
Request redirection
Delayed GC
Background GC
vSSD_ID | GC Status
vSSD | 0
Replica | 0
VSSD_ID | Server IP
vSSD | 10.0.0.16
Replica | 10.0.0.20
vSSD_ID | GC Status
vSSD | 1
Replica | 0
Notify Switch
C
Update switch tables
B
Leverage idle storage cycles for GC
vSSD
Replica
Predict idle time
A

## Slide 19
Enabling Rack-Scale Wear Leveling
Systems Platform Research Group at UIUC
…
Local Wear Leveling
Global Wear Leveling
Increased cost
Increased management complexity
Workload instances have diverse write intensity!
Swap SSDs within servers every 16 days
Swap SSDs across servers every 8 weeks
vSSD
vSSD
vSSD
vSSD
…
Local Wear Leveling
vSSD
vSSD
vSSD
vSSD

## Slide 20
RackBlox Implementation
1 TB
16 Channels
16 KB/page
70 MB/s per channel
TPC-H
TPC-C
AuctionMark
YCSB
Programmable SSDs
Workloads
Programmable Switch
Intel Tofino Switch

## Slide 21
Improving End-To-End I/O Performance
Systems Platform Research Group at UIUC
RackBlox reduces tail latency by up to 4.8x!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
VDC | 1 | 1 | 1 | 1 | 1 | 1
RackBlox-Coord I/O | 0.92915 | 0.89556 | 0.83819 | 0.86744 | 0.99749 | 0.98098
RackBlox (Software) | 0.93341 | 0.91407 | 0.86053 | 0.81081 | 0.41046 | 0.41949
RackBlox | 0.92915 | 0.89556 | 0.83819 | 0.67439 | 0.22686 | 0.22835
Storage!
Networking!

## Slide 22
Systems Platform Research Group at UIUC
RackBlox Supports Different Storage Schedulers
Coordinated I/O Scheduling always outperforms incoordination!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
FIFO | 1 | 1 | 1 | 1 | 1 | 1
RackBlox (FIFO) | 0.85027 | 0.82786 | 0.78454 | 0.78294 | 0.75138 | 0.67542
Deadline | 0.98217 | 0.98836 | 0.97307 | 0.92419 | 0.77723 | 0.77661
RackBlox (Deadline) | 0.86809 | 0.82101 | 0.7839 | 0.73853 | 0.65127 | 0.62912
Kyber | 1.0143 | 0.97262 | 0.90336 | 0.83684 | 0.72552 | 0.68974
RackBlox (Kyber) | 0.85918 | 0.83778 | 0.80101 | 0.75215 | 0.65512 | 0.59714

## Slide 23
RackBlox Summary
Network/Storage Codesign
Improves End-to-End I/O Performance
Ensures Rack-Scale Wear-Balance

## Slide 24
Thank You!
Benjamin Reidys
Yuqi Xue Daixuan Li Bharat Sukhwani
Wen-mei Hwu Deming Chen Sameh Asaad Jian Huang
Systems Platform Research Group

## Slide 25
RackBlox Summary
Network/Storage Codesign
Improves End-to-End I/O Performance
Ensures Rack-Scale Wear-Balance

## Slide 26
Systems Platform Research Group at UIUC
Network Delay
Network Delay
Request #1
Request #2
Storage Delay
Storage Delay
SLO Latency
Enabling Coordinated I/O Scheduling
Storage Delay
Request Delay
Storage Queue
Request #2
I/O Request
I/O Request
Request #1
In-Network Telemetry
Storage Queuing Delay
Sliding Window Predictor
+
+
=
Storage Delay
Notes: Now that we have fully discussed how to decouple and update the storage state between the SDN and SDF, I will present the coordination that this network/storage co-design enables, starting with coordinated I/O scheduling. Requests may arrive at storage servers with different network delays caused by differences in network scheduling or other network factors. Without coordination, the storage server first execute request #2 and delay request #1, which may violate its SLO. Instead, we could prioritize the request #1 in the storage while realizing that the low network delay for request #2 allows us to relax its storage scheduling. To achieve this, we schedule requests locally in a coordinated fashion using the three components that correspond to end-to-end I/O performance: the incoming network delay, the storage delay, and the outgoing network delay. We compute the incoming network delay as the sum of per hop latencies in the switches using In-Network Telemetry available in programmable switches. We estimate the storage delay based on when the request enters the storage queue. We estimate the outgoing network delay through a simple sliding window algorithm using the recent incoming network latencies. Now consider the previous example, request #2 arrives with a low measured and predicted network delay so it is enqueued into the storage queue with low priority. Request #1 arrives with a high network delay and receives higher scheduling priority. The requests are then processed in a coordinated fashion to improve end-to-end performance.

## Slide 27
Improving End-To-End I/O Performance
Systems Platform Research Group at UIUC
RackBlox reduces tail latency by up to 4.8x!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
VDC | 1 | 1 | 1 | 1 | 1 | 1
RackBlox-Coord I/O | 0.92915 | 0.89556 | 0.83819 | 0.86744 | 0.99749 | 0.98098
RackBlox | 0.92915 | 0.89556 | 0.83819 | 0.67439 | 0.22686 | 0.22835
Notes: We breakdown the performance of RackBlox and compare against (1) VDC which provides software based token-bucket rate limiting per I/O Flow enforced for both network and storage at the end-hosts. Next, we compare RackBlox with only I/O scheduling enabled. Finally, we show the performance of RackBlox. We see that coordinated I/O scheduling can outperform and achieves 1.4x speedup on average. However, with higher write rates, we have more intensive GC and therefore coordinated GC is necessary, resulting in nearly 5x speedup.
**See if we can re-plot this in excel in some wonderfully clever way.

## Slide 28
Improving End-To-End I/O Performance
Systems Platform Research Group at UIUC
RackBlox reduces tail latency by up to 4.8x!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
VDC | 1 | 1 | 1 | 1 | 1 | 1
RackBlox-Coord I/O | 0.92915 | 0.89556 | 0.83819 | 0.86744 | 0.99749 | 0.98098
RackBlox | 0.92915 | 0.89556 | 0.83819 | 0.67439 | 0.22686 | 0.22835
Notes: We breakdown the performance of RackBlox and compare against (1) VDC which provides software based token-bucket rate limiting per I/O Flow enforced for both network and storage at the end-hosts. Next, we compare RackBlox with only I/O scheduling enabled. Finally, we show the performance of RackBlox. We see that coordinated I/O scheduling can outperform and achieves 1.4x speedup on average. However, with higher write rates, we have more intensive GC and therefore coordinated GC is necessary, resulting in nearly 5x speedup.
**see if we can use the breakdown figure here.

## Slide 29
Enabling Rack-Scale Wear Leveling
Systems Platform Research Group at UIUC
…
Local Wear Leveling
…
Local Wear Leveling
Global Wear Leveling
Increased cost
Increased management complexity
Each rack runs many heterogeneous workloads!
Cloud Services
Swap SSDs within servers every 16 days
Swap SSDs across servers every 8 weeks
Notes: Finally, let us discuss how we enable coordinated wear-leveling. By default, SSDs maximize their lifetime by evenly distributing erases across the underlying flash blocks. However, workload heterogeneity can cause wear-imbalance not just within the blocks of an SSD, but also between SSDs within a server or between SSDs across servers. This can lead to early SSD failure which increases cost and management complexity. To address this, we propose a two-level hierarchical wear balancing mechanism. Within each server we introduce a local wear balancer that swaps SSDs within the server following a relaxed wear level scheme proposed in our prior work, FlashBlox. An SSD is swapped block by block atomically by pausing the operations for the chosen blocks, reading them into memory, writing them to their new locations, updating the mapping tables, and serving the paused requests. We can guarantee near optimal lifetime by only swapping every 16 days on average. At server level, network bandwidth can cause significant overhead to swapping so we relax the swapping frequency to every 8 weeks. The local and global wear-balancers work together to keep the rack wear-balanced.
**Want to fix the workloads, show the vSSDs above and different workloads..

## Slide 30
Systems Platform Research Group at UIUC
Network Delay
Network Delay
Request #1
Request #2
Storage Delay
Storage Delay
SLO Latency
In-Network Telemetry (INT)
Storage Queuing Delay
Enabling Coordinated I/O Scheduling
Storage Delay
Sliding Window Predictor
Time
Notes: I will first present how we enable coordinated I/O scheduling. Requests may arrive at storage servers with different network delays caused by differences in network scheduling or other network factors. Without coordination, the storage server may prioritize the request with lower network delay without realizing that delaying the other request may violate the SLO. Instead, we could prioritize the delayed request in the storage while realizing that we the low network delay gives us slack time to delay the other request. Through coordination, we can achieve the SLO for both requests. To achieve this, we schedule requests locally in a coordinated fashion using three components. The network delay before arriving at the server, which is computed as the sum of per hop latencies in the switches using In-Network Telemetry. The storage delay, which we can estimate based on when the request enters the storage stack. And the network delay after leaving the server, which we estimate with a simple, yet effective sliding window algorithm that predicts the return latency using the recent network state. Together, this enables the local storage scheduling to incorporate the network state and appropriately prioritize to achieve predictable end-to-end performance.
**Switch to SLO
**one by one in example
**add scheduling/queue diagram.
**Switch formula to something better looking

## Slide 31
Decoupling the Storage Management Across SDN/SDF
Systems Platform Research Group at UIUC
Storage Management in SDN
vSSD_ID | GC Status | Server IP
vSSD1 | 1 | 10.0.0.16
vSSD2 | 0 | 10.0.0.20
vSSD_ID | GC Status | Replica vSSD_ID
vSSD1 | 1 | vSSD12
vSSD2 | 0 | vSSD20
Storage Management in SDF
…
vSSD #1
vSSD #2
vSSD #3
Flash Channels
Benefits from coordination?
State retained in switch?
31
Storage Functions
I/O Scheduling
Garbage
Collection
Wear
Leveling
Bad Block Management
Address Translation
ECC
Notes: Due to the hardware constraints of SDN, we want to keep as much of the local storage management in the SDF. Accordingly, we use the “virtual SSD” or vSSD abstraction, that we proposed in our prior works FlashBlox and BlockFlex, to manage the local SDF. A vSSD groups together a collection of underlying flash channels and virtualizes them. This enables RackBlox to keep the essential functions for local storage management in the server. When decoupling the storage state for coordination between SDN and SDF, we consider two factors. First, whether integrating the storage function into SDN will benefit from coordination or not. Functions such as bad block management, ECC, and address translation do not benefit, so they remain exclusively in the SDF. For the I/O scheduling, GC, and wear-leveling, we determine if coordination requires using switch memory. We identify that only coordinating GC requires switch memory as I/O scheduling can use the packet and wear-leveling happens infrequently. Therefore, we store two tables in the switch to support coordinating GC. The replica table, which maps the vSSD to its current GC status and replica and the destination table that maps the vSSD to its home server. These tables consume at most 1.3 MB of the 10s of MBs of on-chip switch memory.
This one should flow more
We have sdf -> which has all of these storage function -> ecc in device -> vssd encapsulates -> for the remaining that benefit from coord, we check if should be retained in switch, etc… Think this through very carefully.

## Slide 32
Research Problem: Lack of Coordination between SDN/SDF
Systems Platform Research Group at UIUC
Control Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Congestion Control
Read
Write
Erase
Conflicting policies!
Missed opportunities for rack-scale optimization!
Software-Defined Networking
Data Plane
Data Plane
Software-Defined Flash
Redundant effort!
SDN and SDF should coordinate!
Notes: First, we see that both SDN and SDF have I/O scheduling policies. Unfortunately, the scheduling decisions for packets in the network could conflict with the scheduling decisions for those requests in the storage stack. For one, these conflicting scheduling decisions can lead to unpredictable end-to-end performance. Additionally, separately optimizing the SDN and SDF for end-to-end performance results in redundant effort and additional complexity. We also see that certain storage functions could benefit from a global view of the entire rack. For example, wear-leveling, which helps extend SSD lifetime, is currently performed within individual SSDs, but could be extended to the entire rack. Additionally, garbage collection could be coordinated across data replicas in a rack to avoid its performance interference. Without coordination, we miss out on significant opportunities for optimization and leads us to the conclusion that SDN and SDF should coordinate.
**zoom out for gc + wl
**split
**can also preempt sw in that slide

## Slide 33
Enabling Coordinated Garbage Collection
Systems Platform Research Group at UIUC
Replica
vSSD
Storage Request
vSSD_ID | GC Status
vSSD | 1
Replica | 0
vSSD_ID | GC Status
vSSD | 1
Replica | 1
Request redirection
Delayed GC
Background GC
Request GC
VSSD_ID | Server IP
vSSD | 10.0.0.16
Replica | 10.0.0.20
vSSD_ID | GC Status
vSSD | 0
Replica | 0
vSSD_ID | GC Status
vSSD | 0
Replica | 1
Background GC
Notes: TODO: Need some form of lingering text after the animation disappears -> probably want to split this across slides.
Now that we have empowered the local storage to consider the network state in scheduling, we want to allow the network to consider the storage state. Here we leverage the fact that rack-scale storage deploys at least two replicas so one rack another replica to a different rack by default. In this way, we can leverage the data replicas to redirect requests that would see significant delay due to ongoing GC. For incoming read requests, we first check the GC status bit in the table. If the bit is set, we check the replica to ensure it is not performing GC and redirect the request. However, as writes are issued to all replicas, it is possible for both vSSDs to be performing GC and redirection would not reduce tail latency. Therefore, we enable delaying GC in the switch. vSSDs will request to perform GC earlier than usual, giving the switch an opportunity to delay one replica while the other finishes its GC. Later, if the replica is not performing GC, the request is granted. In this fashion we can minimize the overlap in GC and maximize the chance that one data replica is available to serve requests. Finally, we also enable background GC by opportunistically leverage idle cycles with a simple prediction mechanism using the exponential weighted average of prior idle time. With high accuracy, we predict how long we can perform GC and notify the switch directly so it can redirect requests.

## Slide 34
Decoupling the Storage Management
Systems Platform Research Group at UIUC
Storage Server
Storage Management in SDN
vSSD_ID | GC Status | Server IP
vSSD1 | 1 | 10.0.0.16
vSSD2 | 0 | 10.0.0.20
vSSD_ID | GC Status | Replica vSSD_ID
vSSD1 | 1 | vSSD12
vSSD2 | 0 | vSSD20
Storage Management in SDF
…
VSSD #1
VSSD #2
VSSD #3
Flash Channels
Benefits from coordination?
Consumes minimal resources?
34
Notes: TODO change dramatically to the column and guide through the questions->which benefit->do they consume minimal resources?
In order to decouple the storage management between the SDN and SDF, we first need to share the storage state. Due to the hardware constraints, we want to keep as much of the storage management in the local servers as possible and reduce the burden on SDN. Accordingly, we consider two factors. First, whether integrating an SDF function into SDN will benefit from the coordination or not. Second, if yes, the integration should consume minimum precious hardware resources in the switch. Accordingly, we use the “virtual SSD” or vSSD abstraction, that we proposed in our prior works FlashBlox and BlockFlex. A vSSD groups together a collection of underlying flash channels exposed in SDF and virtualizes them. This enables us to easily keep the storage functions with better performance when in the local storage such as bad block management, ECC, and address translation in the SDF. vSSDs can help achieve predictable performance as individual flash channels can be allocated to a specific vSSD, providing hardware isolation. In the switch, we store two tables to support the storage functions that benefit from coordination. The replica table, which maps the vSSD to its current GC status and replica and the destination table to map the vSSD to its home server. These allow the SDN to redirect requests and coordinate GC and consume only 1.3 MB of the 10s of MBs of on-chip switch memory.

## Slide 35
What is Software-Defined Storage?
Systems Platform Research Group at UIUC
Control Plane
I/O Scheduling
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
Address Translation
Data Plane
Read
Write
Erase
Storage Server
Improved resource utilization
Predictable storage performance
Storage software directly manages the internal operations of devices
Notes: TODO split into three slides with ssd background in the middle.
Due to the benefits of software-defined networking, software-defined storage was also developed. Software-defined storage enables data centers to unlock the potential of storage devices by enabling the software to directly interact with them and control their internal operations. One common example of software defined storage is software defined flash or SDF, which builds on top of solid-state drives (SSDs). In order to understand the details of software-defined flash, let me first introduce SSDs, which due to their high performance and decreasing cost, are being increasingly deployed in modern data centers. Each SSD also has a control plane and data plane. The control plane performs storage functions such as address translation, ECC, bad block management, etc. While the data plane executes the read/write/erase operations. Many of these storage functions are necessary due to the unique properties of the flash medium. Wear leveling, which distributes the erases evenly across the underlying flash blocks, is necessary due to the limited erase count before each flash block wears out and is unusable. Garbage collection periodically erases blocks to ensure free blocks are available for out-of-place updates because flash does not support overwrites. This must be done carefully as erase operations are expensive and can add orders of magnitude delay to storage operations. Software-defined flash opens the black box of the SSDs and allows the system to manage these functions. By exposing these functions to the upper-level system, SDF can achieve improved resource utilization and more predictable storage performance.

## Slide 36
Modern Data Centers are Increasingly Software Defined
Systems Platform Research Group at UIUC
Top of Rack (ToR) Switch
Clients
…
Storage Server
Storage Server
Software-Defined
Networking
Software-Defined Storage
Improved
Resource Efficiency
Redefine
Management Policies
Notes: TODO: better symbol for software defined + need to better describe why they are becoming popular.
Essential logical flow -> Increasingly becoming software defined-> defined as control plane + data plane which allows redefining management policies for improved resource efficiency-> Because of these benefits, we saw SDN developed and later, SDS->deployed in Google data centers, Alibaba, etc.
Modern data center infrastructure is increasingly software-defined where each component has a control plane that defines the policies and a data plane that executes them. By making infrastructure software-defined, we achieve two major benefits. First, we achieve the flexibility to redefine the policies of the control plane to quickly adapt to data center needs. Second, we can define customized policies that optimize resource efficiency.
Missing why.

## Slide 37
COMPUTER SCIENCE
Managing Data Center Storage at Rack-Scale
Systems Platform Research Group at UIUC
Top of Rack (ToR) Switch
Clients
…
Storage Server
Storage Server
Software-Defined
Networking
Software-Defined Storage
Improved
Resource Utilization
Simplified
Resource Management
Notes: In order to provide storage services, data centers manage storage at rack scale.

## Slide 38
COMPUTER SCIENCE
What is Software-Defined Networking?
Systems Platform Research Group at UIUC
Control Plane
Data Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Congestion Control
Software-Defined Networking
Programmable Switches
Customized Network Functions
Hardware Constraints
Control Plane
Address Translation
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
I/O
Scheduling
Data Plane
Read
Write
Erase
Storage Server
Software-Defined Storage
Notes: Data centers adopted software defined networking and software defined storage for the flexibility such as in scheduling and resource management. For networking, this is achieved…
Make new slide with new title: “SDN/SDF are managed separately”… makes sense on face.

## Slide 39
COMPUTER SCIENCE
Software-Defined Storage Infrastructure
Systems Platform Research Group at UIUC
Control Plane
Address Translation
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
I/O
Scheduling
Data Plane
Read
Write
Erase
Storage Server
Software-Defined Storage
Empowered Storage Software
Improved Resource Efficiency
Control Plane
Data Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Congestion Control
Software-Defined Networking
Notes: Due to the success of software defined networking, software defined storage was also developed.

## Slide 40
COMPUTER SCIENCE
Challenges in Modern Software-Defined Infrastructure
Systems Platform Research Group at UIUC
Control Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
Address Translation
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
I/O
Scheduling
Congestion Control
Read
Write
Erase
Incoordination!
Could benefit from global view!
Coordinated I/O
Scheduling
Local I/O
Scheduling
Coord. Garbage
Collection
Global Wear
Leveling
Local Garbage Collection
Local Wear Leveling
Software-Defined Networking
Data Plane
Data Plane
Software-Defined Storage
Notes: Unfortunately, modern data centers manage SDN and SDF separately, which leads to suboptimal end-to-end storage performance.

## Slide 41
COMPUTER SCIENCE
Lack of Coordination in Modern Software-Defined Infrastructure
Systems Platform Research Group at UIUC
Control Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
Address Translation
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
I/O
Scheduling
Congestion Control
Read
Write
Erase
Incoordination!
Could benefit from global view!
Software-Defined Networking
Data Plane
Data Plane
Software-Defined Storage
SDN and SDF should coordinate!
Notes: Unfortunately, modern data centers manage SDN and SDF separately, which leads to suboptimal end-to-end storage performance.
Change the icons to icons that represent the bad things that will happen without coordination:
unpredictability.
Redundant effort -> complications
Missed optimization opportunity.

## Slide 42
COMPUTER SCIENCE
Achieving Network/Storage Codesign with RackBlox
Systems Platform Research Group at UIUC
Limited Hardware Resources
Ensure flexibility and
ease-of-use
Decoupling storage management between SDN and SDF
SDF
SDN
Storage Management
Custom Table and Packet Format
+
Decouples Coordination from
Specific Policies
Careful Function Coordination
SDN Management
SDF Management
SDF Management
Notes: Transition from the previous slide and include the high level description of

## Slide 43
COMPUTER SCIENCE
Systems Platform Research Group at UIUC
Network Latency
Network Latency
Request #1
Request #2
Storage Latency
Storage Latency
Tail Latency Violation!
Coordination
Network Latency
Network Latency
Request #1
Request #2
Storage Latency
Storage Latency
Tail Latency Guaranteed!
In-Network Telemetry (INT)
Storage Queuing Delay
Enabling Coordinated I/O Scheduling
Notes: Want to discuss the potential of coordinated scheduling, how we define the time, and how track/predict the time
Net time comes from INT, storage time comes from queuing delay, predict time comes from expected return time which we predict.

## Slide 44
COMPUTER SCIENCE
Enabling Coordinated GC
Systems Platform Research Group at UIUC
Replica
vSSD
Storage Request
vSSD_ID | GC Status
vSSD | 1
Replica | 0
vSSD_ID | GC Status
vSSD | 1
Replica | 1
Request Redirection
Delayed GC
Background GC
Request GC
VSSD_ID | Server IP
vSSD | 10.0.0.16
Replica | 10.0.0.20

## Slide 45
COMPUTER SCIENCE
Enabling Coordinated Wear Leveling
Systems Platform Research Group at UIUC
Storage Server
…
Local
Storage Server
…
Local
Global
Heterogeneous Workloads!
Increased Cost
Increased Management Complexity
Achieves Rack-Scale Wear-Balance!

## Slide 46
COMPUTER SCIENCE
Storage is a Core Data Center Infrastructure
Systems Platform Research Group at UIUC
Data Center Storage
Cloud Services
Notes: Data center storage is a core service that underpins many critical data center workloads such as database workloads, AI, and other cloud services, storing thousands of exabytes in total.

## Slide 47
COMPUTER SCIENCE
Modern Software-Defined Infrastructure
Systems Platform Research Group at UIUC
Control Plane
Data Plane
L2/L3 Routing
Data
Cache
Network Statistics
I/O
Scheduling
Control Plane
Address Translation
Garbage
Collection
Wear
Leveling
ECC
Bad Block Management
I/O
Scheduling
Data Plane
Congestion Control
Read
Write
Erase
Storage Server
Software-Defined Networking
Software-Defined Storage
Notes: Data centers adopted software defined networking and software defined storage for the flexibility such as in scheduling and resource management.

## Slide 48
COMPUTER SCIENCE
Enabling Coordinated GC
Systems Platform Research Group at UIUC
Replicas may GC concurrently!
Still want to minimize GC occurrences!
Request Redirection
Delayed GC
Background GC
Notes: ****This needs to be redrawn****

## Slide 49
COMPUTER SCIENCE
Network/Storage Co-Design is Promising
Systems Platform Research Group at UIUC
GC increases request tail latency by over 5x!
Requests spend nearly equal time in network and storage!

## Slide 50
COMPUTER SCIENCE
Systems Platform Research Group at UIUC
Sensitivity Study of Network/Storage Latency
Best improvement when variation and latencies match!
Notes: The diagonal has the best performance.

## Slide 51
COMPUTER SCIENCE
Systems Platform Research Group at UIUC
Coordinated Wear-Leveling
RackBlox ensures rack-scale wear-balance!
Notes: 8 week default gives roughly 1.2x imbalance.

## Slide 52
Improving End-To-End Performance
Systems Platform Research Group at UIUC
RackBlox reduces tail latency by up to 4.8x!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
VDC | 1 | 1 | 1 | 1 | 1 | 1
NetFlash-Coord I/O | 0.92915 | 0.89556 | 0.83819 | 0.86744 | 0.99749 | 0.98098
NetFlash | 0.92915 | 0.89556 | 0.83819 | 0.67439 | 0.22686 | 0.22835
Notes: **TODO switch this to RackBlox.
We breakdown the performance of RackBlox and compare against (1) VDC which provides software based token-bucket rate limiting per I/O Flow enforced for both network and storage at the end-hosts. Next, we compare with RackBlox with only I/O scheduling enabled. Finally, we show the performance of RackBlox. We see that coordinated I/O scheduling can outperform and achieves 1.4x speedup on average. However, with higher write rates, we have more intensive GC and therefore coordinated GC is necessary, resulting in nearly 5x speedup.

## Slide 53
Systems Platform Research Group at UIUC
Flexibility for Supporting Different Storage Schedulers
Coordinated I/O Scheduling always outperforms incoordination!
Chart: Read/Write Mix (%)
| 100/0 | 95/5 | 80/20 | 50/50 | 20/80 | 5/95
FIFO | 1 | 1 | 1 | 1 | 1 | 1
NetFlash (FIFO) | 0.85027 | 0.82786 | 0.78454 | 0.78294 | 0.75138 | 0.67542
Deadline | 0.98217 | 0.98836 | 0.97307 | 0.92419 | 0.77723 | 0.77661
NetFlash (Deadline) | 0.86809 | 0.82101 | 0.7839 | 0.73853 | 0.65127 | 0.62912
Kyber | 1.0143 | 0.97262 | 0.90336 | 0.83684 | 0.72552 | 0.68974
NetFlash (Kyber) | 0.85918 | 0.83778 | 0.80101 | 0.75215 | 0.65512 | 0.59714
Notes: **TODO switch this to RackBlox.
To demonstrate the flexibility, we isolate the benefits of coordinated I/O scheduling when integrating it into different schedulers that Linux offers today, base FIFO (or no-op), deadline, and Kyber, which have different methods of targeting low latency storage requests. We see that coordination improves each one scheduler significantly achieving 1.4x improvements on average across different read/write ratios.

## Slide 54
COMPUTER SCIENCE
Filler
Systems Platform Research Group at UIUC